## Slide 1
Clustering Heavy Duty Truck Failure Modes for Proactive Safety Inspection and Efficient Operations of Commercial Vehicle Fleets
Chenyu Yuan
Presentation at the 7th Annual UTC Conference for the Southeastern Region in Boca Raton, FL

## Slide 2: Content
Motivation and Introduction
Data Sources
Current Practice
Conclusion and Future Work

## Slide 3: Motivation and Introduction
Historical Truck Inspection Data
Historical Truck Crash Data
Real-time Telematics Data (under permission)
Cluster
Explore different failure mode for different groups of vehicles
Predict the potential risks compared with FMCSA vehicle maintenance criteria
Basic Feature Importance Selection
FMCSA Satisfactory Indicator
Compare
Set up a data collection plan for fleet and carrier
feedback
Design
A user-interactive dashboard
Statistical fact of fleet performance
Cost/Safety-Oriented Consultant

## Slide 4: Data Sources
Compuspections
MCMIS Database (From Federal Motor Carrier Safety Administration)
MCMIS Database (From Federal Motor Carrier Safety Administration)

## Slide 5: Current Practice – Data Preprocessing
5
1. Background Information
2. Key Component Failure Information
3. Key Component Failure Information but with large pieces of missing
5 Different Datasets:
A: Only 1
B: Only 2
C: 2 + 3
D: 1 + 2
E: 1 + 2 + 3

## Slide 6: Current Practice – K-means Algorithm
Basic Data Statistics
Data Standardization and Clusterable Evaluation
K Value Estimation
Cluster Evaluation

## Slide 7: Current Practice – K-means Algorithm
Basic Data Statistics
Data Standardization and Clusterable Evaluation
K Value Estimation
Cluster Evaluation

## Slide 8: Current Practice – K-means Algorithm
Data Standardization and Clusterable Evaluation
K Value Estimation
Cluster Evaluation
Basic Data Statistics
Hopkins Statistics
Step 1: Let X be the set of n data points, consider a random smaple (without replacement) of m << n data points with members .
Step 2: Generate a set Y of m uniformly randomly distributed data points.
Step 3: Define two distance measures: . The distance of from its nearest neighbour in Y
. The distance of m number of randomly chosen from its nearest neighbour in X
With the above notation, if the data is d dimensional, then the Jopkins statistics is defined as:
A value close to 1 tends to indicate the data is highly clustered, random data will tent to result in values around 0.5, and uniformly distributed data will tent to result in values close to 0.
Notes: Source: https://en.wikipedia.org/wiki/Hopkins_statistic

## Slide 9: Current Practice – K-means Algorithm
Data Standardization and Clusterable Evaluation
K Value Estimation
Cluster Evaluation
Basic Data Statistics
Dataset A | 0.97872
Dataset B | 0.99932
Dataset C | 0.99851
Dataset D | 0.97394
Dataset E | 0.97394
Notes: Source: https://en.wikipedia.org/wiki/Hopkins_statistic

## Slide 10: Current Practice – K-means Algorithm
K Value Estimation
Cluster Evaluation
Basic Data Statistics
Data Standardization and Clusterable Evaluation
For Dataset B:
Given Dataset , every sample point
K-means algorithm is trying to classify n data points in to k different cluster , and for each S, sample point in Cluster S has the minimum WCSS (within-cluster sum of squares).
K value Selection: Elbow method （肘部法）
K = 3 or 6 might be the best values for K
Notes: Source: https://en.wikipedia.org/wiki/Hopkins_statistic

## Slide 11: Current Practice – K-means Algorithm
K Value Estimation
Cluster Evaluation
Basic Data Statistics
Data Standardization and Clusterable Evaluation
For Dataset B:
K value Evaluation: Silhouette Coefficient （轮廓系数）
For data point (data point I in the cluster ), let
be the mean distance between i and all other data points in the same cluster, where is the number of points belonging to cluster i, and d(i, j) is the distance between data points I and j in the cluster (we divide by - 1 because we do not include the distance d(i, i) in the sum). We can interpret a(i) as a measure of how well I is assigned to its cluster (the smaller the value, the better the assignment)
We then define the mean dissimilarity of point to some cluster as the mean of the distance from I to all points in (where )
For each data point , we now define
to be the smallest (hence the min operator in the formula) mean distance of i to all points in any other cluster, of which i is not a member.
Notes: Source: https://en.wikipedia.org/wiki/Hopkins_statistic

## Slide 12: Current Practice – K-means Algorithm
K Value Estimation
Cluster Evaluation
Basic Data Statistics
Data Standardization and Clusterable Evaluation
For Dataset B:
K value Evaluation: Silhouette Coefficient
S(i) ranges from -1 to +1, where a high value indicates that the object is well matched to its own cluster , and the lower value indicates that the object is poorly matched to its own cluster.
Cluster | Silhouette Score
3 | 0.904
6 | 0.928
Notes: Source: https://en.wikipedia.org/wiki/Hopkins_statistic

## Slide 13: Current Practice – K-means Algorithm
K = 3 Classification:
 | Registration | Doors | Lighting | Steering | Exhaust | Fuel | Glazing | Other | Brakes | RoadTest | Tires | Conclusion
Cluster Category | failure_rate | failure_rate | failure_rate | failure_rate | failure_rate | failure_rate | failure_rate | failure_rate | failure_rate | failure_rate | failure_rate | 
0 | 0.01108801 | 0.05682606 | 1 | 0.13444213 | 0.17325017 | 0.02286902 | 0.03534304 | 0.23562024 | 0.41926542 | 0.04019404 | 0.11503812 | Vehicles with Lighting Failure and some problems with other components and brakes
1 | 0.00074269 | 0.00111403 | 0 | 0.00495126 | 0.0070246 | 0.00105214 | 0.00077363 | 0.00912889 | 0 | 0.00030945 | 0.00810769 | Vehicles with no or few problems
2 | 0.00169924 | 0.02039082 | 0 | 0.13338997 | 0.14273577 | 0.01869159 | 0.01104503 | 0.17247239 | 1 | 0.01359388 | 0.10790144 | Vehicles with brakes problem
Notes: Source: https://en.wikipedia.org/wiki/Hopkins_statistic

## Slide 14
K = 6 Classification:
 | Registration | Doors | Lighting | Steering | Exhaust | Fuel | Glazing | Other | Brakes | RoadTest | Tires | Conclusion
Cluster Category | failure_rate | failure_rate | failure_rate | failure_rate | failure_rate | failure_rate | failure_rate | failure_rate | failure_rate | failure_rate | failure_rate | 
0 | 0.00056618 | 0.00081782 | 0 | 0.00396326 | 0.00512708 | 0.00081782 | 0.00050327 | 0 | 0 | 0 | 0 | No problems
1 | 0.01322314 | 0.07933884 | 1 | 0.20826446 | 0.2446281 | 0.0231405 | 0.04958678 | 0.30247934 | 1 | 0.0661157 | 0.13057851 | Vehicles with both lighting and brakes problem, while steering and exhaust problems might occur
2 | 0.00954654 | 0.04057279 | 1 | 0.08114558 | 0.12171838 | 0.02267303 | 0.02505967 | 0.18735084 | 0 | 0.02147971 | 0.10381862 | Vehicles with lighting problems but without any brakes problem
3 | 0.00537634 | 0.0188172 | 0 | 0.04301075 | 0.13709677 | 0.02150538 | 0.00537634 | 0.08602151 | 0.30107527 | 0.01075269 | 1 | Vehicles without any lighting problems but with tires problem, brakes problem might occur
4 | 0.00858369 | 0.04291845 | 0 | 0.16094421 | 0.16309013 | 0.01287554 | 0.0193133 | 1 | 0.43562232 | 0.0472103 | 0.03648069 | Vehicles without any lighting problems but with other components problems, brakes, steering and exhaust problems might occur
5 | 0.00232019 | 0.00812065 | 0 | 0.11600928 | 0.12180974 | 0.01856148 | 0.01276102 | 0 | 1 | 0 | 0 | Vehicles without any lighting, other components, roadtest and tires problems but with brakes problem
Current Practice – K-means Algorithm
Notes: Source: https://en.wikipedia.org/wiki/Hopkins_statistic

## Slide 15: Current Practice – K-means Algorithm
Visualization Method: t-SNE
Given a set of N high-dimensional objects, …, , t-SNE first computes probabilities that are proportional to the similarity of objects and
T-SNE aims to learn a d-dimensional map , …, that reflects the similarities as well. So it uses to reflect similarities between two points in the map and using a very similar approach
And we also use student-t distribution to measure similarities between high dimensional similarities and low dimensional similarities. The locations of the points in the map are determined by minimizing the Kullback-Leiber divergence of the distribution P from distribution Q
Notes: Source: https://en.wikipedia.org/wiki/Hopkins_statistic

## Slide 16
Current Practice – K-means Algorithm
0 | 494
1 | 13602
2 | 368
Numbers of vehicle in different Classification
0 | 13437
1 | 219
2 | 272
3 | 107
4 | 156
5 | 273
Notes: Source: https://en.wikipedia.org/wiki/Hopkins_statistic

## Slide 17: References
[1] https://www.cnblogs.com/ljhdo/p/5556635.html
[2] https://www.i4k.xyz/article/swy_swy_swy/106109004
[3] https://blog.csdn.net/tszupup/article/details/84997804
[4] Francisco C. Pereira, Filipe Rodrigues, Moshe Ben-Akiva, Text analysis in incident duration prediction, Transportation Research Part C: Emerging Technologies, Volume 37, 2013, Pages 177-192, ISSN 0968-090X, https://doi.org/10.1016/j.trc.2013.10.002.
[5] http://www.datakit.cn/blog/2017/02/05/t_sne_full.html