Cover Page

Submission number: 64

A DATA-DRIVEN ASSESSMENT OF SAFETY INSPECTION PROGRAMS’ EFFICACY

Prithvi S. Acharya a,  H. Scott Matthews a,b,

a Department of Engineering & Public Policy, Carnegie Mellon University, USA

b Department of Civil and Environmental Engineering, Carnegie Mellon University, USA

Email: acharyap@cmu.edu

Email: hsm@cmu.edu

Abstract

Fifteen U.S. states currently require vehicles to undergo periodic safety inspections, to ensure safe tire tread-depth, functioning lights, mirrors and wipers, etc. The effectiveness of these programs has been called into question by several legislatures; since 2000, four of these states have repealed their inspection programs, finding them not to be cost-effective. Applying statistical models to data from the publicly available Fatality Analysis Reporting System (FARS), we analyze the impact of the abolition of safety inspections in these states, on the occurrence of fatal road accidents. We find that on average, the mean number of road fatalities per unit population was higher, five years following the repeal than two years prior. We also propose a generic model to estimate the potential impact of instating or repealing a safety inspection program for a given vehicle population.

Keywords: Vehicle safety, I/M Programs, FARS, statistical analysis

Subject area: (Please put a “X” as appropriate, you may choose more than one)

| X | a) | Smart Mobility |
| --- | --- | --- |
|  | b) | Transport and Climate Change |
|  | c) | Logistics and Supply Chain Management |
| X | d) | Transportation, Society, and People |
|  | e) | Transportation, Land Use, and Built Environment |
|  | f) | Regional and International Transportation |
|  | g) | Public Transport |
|  | h) | Transport Modelling and Surveys |
|  | i) | Networks |
| X | j) | Transport Infrastructure |

Preferred mode of presentation: (Please put a “X” as appropriate)

| X | Oral presentation only |  | Poster presentation only |
| --- | --- | --- | --- |
|  | No preference |  |  |

Name of presenter/key speaker:

Prithvi S. Acharya

Request for the consideration of publication in the Proceedings: (Please put a “X” as appropriate)

|  | Presentation and Publication | X | Presentation only |
| --- | --- | --- | --- |

Submission for HKSTS Outstanding Student Paper Award (You are a postgraduate student and the SOLE author of the paper): (Please put a “X” as appropriate)

|  | Yes | X | No |
| --- | --- | --- | --- |

A DATA-DRIVEN ASSESSMENT OF SAFETY INSPECTION PROGRAMS’ EFFICACY

Prithvi S. Acharya a,  H. Scott Matthews a,b,

a Department of Engineering & Public Policy, Carnegie Mellon University, USA

b Department of Civil and Environmental Engineering, Carnegie Mellon University, USA

Email: acharyap@cmu.edu

Email: hsm@cmu.edu

Abstract

Fifteen U.S. states currently require vehicles to undergo periodic safety inspections, to ensure safe tire tread-depth, functioning lights, mirrors and wipers, etc. The effectiveness of these programs has been called into question by several legislatures; since 2000, four of these states have repealed their inspection programs, finding them not to be cost-effective. Applying statistical models to data from the publicly available Fatality Analysis Reporting System (FARS), we analyze the impact of the abolition of safety inspections in these states, on the occurrence of fatal road accidents. We find that on average, the mean number of road fatalities per unit population was higher, five years following the repeal than two years prior. We also propose a generic model to estimate the potential impact of instating or repealing a safety inspection program for a given vehicle population.

Keywords: Vehicle safety, I/M Programs, FARS, statistical analysis

# INTRODUCTION

Technological advances, and safety regulations continue to improve the safety of new light-duty motor vehicles (LDV’s). However, routine maintenance—to ensure proper tire tread-depth, effective brakes, functioning lights, etc.,—is critical to the continued safe operation of LDV’s. To ensure adherence to these safety requirements, many jurisdictions (including all E.U. member nations) administer vehicle inspection and maintenance (I/M) programs. Typically, these programs require vehicles to be inspected periodically, and only certified as road-legal after the completion of requisite maintenance to ensure they are safe to operate. In the United States, safety inspection programs (which are managed at the state-level) have received significant political opposition over the last half-century, leading to the abolition of I/M programs in several states. Figure 1 shows that while there were 32 states with I/M programs in the mid-1970’s, more than half of these states have since repealed the programs. Much of this opposition posits that inspection programs are not an effective means of preventing road fatalities and are therefore a waste of time and money for vehicle-owners and administrative authorities.

As jurisdictions continue to debate the need for I/M programs, it is imperative that statistical analyses be conducted to assess the effectiveness of safety inspection programs, in achieving their stated aim of preventing road fatalities. Merrell et al. (1999) have applied econometric tools to assess the effectiveness of safety inspection programs, and while they concluded that I/M programs may not have any effect on fatality rates, their analyses are based on data from the 1970’s and 80’s, and do not benefit from more recent data. As a counterpoint, a time-series analysis conducted by Loeb and Gilad (1984), found the benefits of vehicle inspection programs to outweigh the costs. Other literature published around this time have all used limited datasets and had a high degree of variability in their conclusions on the effectiveness of safety inspection programs (Garbacz, 1990; Loeb, 1990). Sutter and Merrell (2002), go so far as to argue that safety inspections have absolutely no impact on highway safety, and that the states which continue to administer these programs do so purely due to the high “political transaction cost” of repealing them.

A more recent assessment of the abolition of New Jersey’s I/M program asserted that there was no link between program repeal and fatal accident rates (Hoagland and Woolley, 2018). However, as discussed further in Section 2, our analyses differ from past literature in scope and methods. Unlike early studies, our research uses up-to-date, publicly available raw data on fatal motor vehicle accidents, from the U.S. Department of Transportation. Second, rather than focusing on accidents in any one specific state, we intend to apply a pooled regression (and other panel data approaches) to data from every state in the country, allowing us to develop a more robust estimate of the population-adjusted rate of road-accident related fatalities, as a function of the presence or absence of an I/M program in that state. Third, and most importantly, our study considers the long-term effects of establishing or repealing an I/M program, rather than only the immediate effects, as is typical in the literature.

Figure 1: Since 1976, 17 U.S. states have repealed I/M programs

Table I: Nationwide annual road-fatalities have decreased steadily over time.

| Year | Fatal Accidents | Vehicles Recorded | Persons Recorded | Total Fatalities |  | Year | Fatal Accidents | Vehicles Recorded | Persons Recorded | Total Fatalities |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1988 | 42,130 | 62,703 | 112,958 | 47,087 |  | 2003 | 38,477 | 58,877 | 101,862 | 42,884 |
| 1989 | 40,741 | 60,870 | 109,866 | 45,582 |  | 2004 | 38,444 | 58,729 | 100,760 | 42,836 |
| 1990 | 39,836 | 59,292 | 107,777 | 44,599 |  | 2005 | 39,252 | 59,495 | 101,262 | 43,510 |
| 1991 | 36,937 | 54,795 | 99,369 | 41,508 |  | 2006 | 38,648 | 58,094 | 98,356 | 42,708 |
| 1992 | 34,942 | 52,227 | 95,691 | 39,250 |  | 2007 | 37,435 | 56,253 | 94,338 | 41,259 |
| 1993 | 35,780 | 53,777 | 97,589 | 40,150 |  | 2008 | 34,172 | 50,660 | 84,510 | 37,423 |
| 1994 | 36,254 | 54,911 | 98,945 | 40,716 |  | 2009 | 30,862 | 45,540 | 76,510 | 33,883 |
| 1995 | 37,241 | 56,524 | 102,102 | 41,817 |  | 2010 | 30,296 | 44,862 | 74,863 | 32,999 |
| 1996 | 37,494 | 57,347 | 103,347 | 42,065 |  | 2011 | 29,867 | 44,119 | 73,364 | 32,479 |
| 1997 | 37,324 | 57,060 | 102,197 | 42,013 |  | 2012 | 31,006 | 45,960 | 76,436 | 33,782 |
| 1998 | 37,107 | 56,922 | 101,100 | 41,501 |  | 2013 | 30,202 | 45,101 | 74,331 | 32,893 |
| 1999 | 37,140 | 56,820 | 100,666 | 41,717 |  | 2014 | 30,056 | 44,950 | 73,711 | 32,744 |
| 2000 | 37,526 | 57,594 | 100,716 | 41,945 |  | 2015 | 32,538 | 49,478 | 81,620 | 35,484 |
| 2001 | 37,862 | 57,918 | 101,175 | 42,196 |  | 2016 | 34,748 | 52,714 | 86,474 | 37,806 |
| 2002 | 38,491 | 58,426 | 101,784 | 43,005 |  | 2017 | 34,247 | 52,645 | 84,921 | 37,133 |

# DATA

The United States National Highway Traffic Safety Administration (NHTSA) administers a database through the Fatality Analysis Reporting System (FARS), which has, since 1976, collected data on motor-vehicle accidents anywhere in the United States, which resulted in at least one fatality. FARS contains information on each accident (location, weather and road conditions, number of vehicles involved, etc.,), in addition to information on individual vehicles involved in these accidents (make and age, vehicle-related contributing factors to the accident, speed, etc.,), as well as demographic information of drivers, passengers and pedestrians. More details, including a full list of fields in the FARS data is available in NHTSA’s Analytical User Manual (NHTSA, 2016). The models presented below were developed from thirty years’ FARS, from 1988 to 2017 (the most recent year for which FARS data are available). During this time, five U.S. states and the District of Columbia repealed their I/M programs.  Table I lists some descriptive statistics from these data and shows that the total number of road fatalities have been rather consistently, if slowly, reducing over time. In 2017, 37,133 fatalities were reported nationwide, resulting from 34,247 accidents.

# METHODS

The stated aim of most I/M programs is to reduce fatalities from road accidents by ensuring that vehicles are safe to operate. Therefore, we develop models which aim to assess whether there is any correlation between the presence of an I/M program in a state, and the number of fatalities involving vehicles registered in that state, each year. Specifically, we develop regression models against the population adjusted number of annual statewide fatalities, represented in fatalities per 100,000 population (Equation 1).

Equation 1

It must be noted that while the analyses we conduct are at the state-level, the “state” considered is not the state in which the fatal accident occurred, but in-fact the state to which each vehicle involved in the accident was registered. As discussed in more detail by Hoagland & Wooley (2018), this approach accounts for the fact that vehicles are regulated (and specifically, subject to inspections) based on the state in which they are registered, regardless of where the vehicle was when an accident occurred. Since FARS provides time-series for accidents in each of the fifty states, over a long duration, we developed regressors by-year and by-state, and applied panel data methods to these regressors. Both variations of the model presented in this paper are independently pooled data models. Pooled models were selected since regulations vary between states, and since we assume that the fatality rates in each state and year are independent of fatality rates in other states or years.

## REGRESSORS

In order to develop a panel data type regression model, where the predicted variable is the adjusted fatality rate, as discussed above, we developed a number of regressors (by-year and by-state), which are listed in Table II. Using these regression features, we developed two variations on a pooled panel data model as discussed in sections 3.2 and 3.3.

## FIRST REGRESSION MODEL

We develop a pooled panel data model, regressing every regressor discussed in Table II, against the adjusted fatality rate.

## LAGGED BINARY VARIABLE

We hypothesize that should the repeal (or institution) of an I/M program have an impact on the adjusted fatality rate, it would not manifest until at least one year after the repeal. This is because for the first year after the program repeal, most vehicles would likely have been inspected (and if needed, repaired) in the preceding year (or in states with biennial inspection programs, two years). As vehicles are uninspected for longer periods of time, we hypothesize an increased likelihood of unsafe vehicles plying the roads, and potentially, some resultant impact on the adjusted fatality rate. To assess this, we tested variations of the first model (described in section 3.2), where, the binary regressor corresponding to the presence of an I/M program was altered by lagging this binary variable by one to ten years. In real terms, a lag of x years on the regression variable indicates whether the state in question had an active I/M program x years ago. For each of these model runs, we evaluated the coefficient and p-value associated with the lagged regressor, as well as the overall R2 value of the model itself.

Table II: Panel regression features were developed from FARS data.

| Feature | Data Source | Notes |
| --- | --- | --- |
| Vehicle mean age | FARS | From vehicles in the FARS database for a given year, which are registered in the given state. |
| Mean age of driver |  |  |
| Mean number of vehicles in each accident |  |  |
| Proportion of vehicles with listed "contributing vehicle failure". |  |  |
| Proportion of vehicles involved in a DUI-related accident |  |  |
| Proportion of vehicles involved in speeding-related accident |  |  |
| Mean number of lanes at accident site |  |  |
| Proportion of vehicles involved in accident during recorded inclement weather |  |  |
| VMT per capita | NHTSA (VM-202) |  |
| Proportion of VMT on rural roads |  |  |
| Active I/M program? | GAO 2015 | Binary variable (1 = program exists, 0 = no program) |

## FINAL MODEL

To construct our final model, we made two primary changes from the first model described in section 3.2. Since, in that model, two variables, we excluded them from the final model.  Second, based on the analysis described in section 3.3, we lagged the binary variable corresponding to the presence of an I/M program, by five years, to minimize the term’s p-value and maximize its regression coefficient. The final model was therefore a pooled panel data model, regressing six variables from FARS, and the lagged binary variable discussed in section 3.3 against the adjusted fatality rate (fatalities/100,000pop).

# RESULTS

The results from the first model, presented in Table III, show that nine out of the eleven regressors considered appear to have a statistically significant relationship with our dependent variable. The most significant positive effect (increase in adjusted fatality rate with increase in regressors) appears to be from the proportion of miles driven on rural roads. The presence of an I/M program also showed a negative effect of -0.86. This can be interpreted as that the presence of a safety inspection program in that state reduces the number of fatalities in a given year by 0.86 fatalities/100,000 population. It is worth noting in this model that the coefficients for the proportion of accidents where inclement weather were recorded, are negative (indicating that, as per the model, when an increased proportion of vehicles registered in a state are involved in accidents due to inclement weather, the adjusted fatality rate reduces). This is a counter-intuitive finding and warrants further analysis. However, based on this first model, it appears that two variables – mean vehicle age, and mean number of vehicles involved in each accident, were found to not be significant (p < 0.05). Therefore, these two variables were excluded from analysis in the final model.

Table III: In the first model, several regressors were found to be significant.

| Predictors | Estimates | CI | p-value |
| --- | --- | --- | --- |
| (Intercept) | 6.41 | -2.28 – 15.10 | 0.149 |
| Vehicle Mean Age | 0.01 | -0.35 – 0.37 | 0.967 |
| Mean Number of Vehicles in Accident | -2.66 | -5.83 – 0.51 | 0.101 |
| Proportion w/ DUI | 5.69 | 0.31 – 11.07 | 0.039 |
| Proportion w/ Contributing Vehicle Failure | -23.21 | -42.15 – -4.26 | 0.017 |
| Mean Number of Lanes | 3.36 | 1.62 – 5.10 | <0.001 |
| Proportion w/ Speeding | -7.63 | -12.26 – -3.01 | 0.001 |
| Proportion w/ Inclement Weather | -10.98 | -16.18 – -5.77 | <0.001 |
| Mean Driver Age | -0.2 | -0.28 – -0.12 | <0.001 |
| Proportion of VMT on Rural Roads | 13.84 | 11.04 – 16.65 | <0.001 |
| VMT Per Capita | 0.01 | 0.01 – 0.01 | <0.001 |
| Active IM Program? (Binary Variable) | -0.86 | -1.71 – -0.01 | 0.048 |
| Dependent Variable: | Fatalities/100,000 Population |
| Observations: | 409 |  |  |
| R2 / R2 adjusted | 0.689 / 0.680 |  |

Results from the analysis described in section 3.3 (where, the model described above was altered by lagging the binary variable representing the presence of I/M programs) are presented in Figure 2, which shows that model R2 appears to increase (if only slightly), with higher lags. The figure also clearly shows that when  the variable is lagged five years (i.e., representing the question ‘did this state have an I/M program five years ago?’) the p-value for that particular binary variable within the model is lowest, and the magnitude of the coefficient estimate for that variable is the highest. While further analyses are required, this potentially indicates that highest effect of repealing an inspection program, on adjusted fatality rates, may only be five years after vehicles stop being inspected. However, the regressors were found to be significant (p < 0.05) for all the first seven lagged terms, indicating that adjusted fatality rates could be affected from the year of repeal through seven years.

Figure 2: At a lag value of 5 years, the magnitude of the estimated coefficient is maximized.

Our final model shows (Table IV) that several of our regression variables may be statistically significant. Here too, there is a counter-intuitive, negative effect of recorded instances of speeding and inclement weather, which warrant further analysis. The highest positive effects (i.e., regressors correlated to an increase in adjusted fatality rate) were attributable to the proportion of miles typical drivers in each state drive on rural roads (vs. urban roads and highways), followed by the proportion of fatal accidents involving drivers under the influence of alcohol or drugs (DUI). Regarding the presence of I/M programs, the lagged term (i.e., was there an active I/M program in this state five years ago) was found with a high confidence (p < 0.01) to have a negative impact on adjusted fatality rates, with a coefficient estimate between -0.42 and -1.97. This may be interpreted to mean that in states which had an inspection program five years before any year being analyzed, the number of road fatalities may be expected to be between 0.42 and  1.97 fewer per 100,000 citizens, than if the state did not have an inspection program. In real terms, for a state such as New Jersey (2017 population, 9.01 million), repealing an existing program could lead to 38-178 additional deaths in the fifth year after the program has been repealed.

Table IV: Final model shows I/M  programs to be a significant predictor of adjusted fatality rate.

| Predictors | Estimates | CI | p-value |
| --- | --- | --- | --- |
| (Intercept) | -0.27 | -6.92 – 6.38 | 0.937 |
| Proportion w/ DUI | 3.93 | -1.61 – 9.48 | 0.166 |
| Proportion w/ Contributing Vehicle Failure | -21.45 | -40.79 – -2.10 | 0.03 |
| Mean Number of Lanes | 3.07 | 1.38 – 4.75 | <0.001 |
| Proportion w/ Speeding | -5.45 | -9.59 – -1.32 | 0.01 |
| Proportion w/ Inclement Weather | -10.15 | -14.66 – -5.64 | <0.001 |
| Mean Driver Age | -0.16 | -0.24 – -0.09 | <0.001 |
| Proportion of VMT on Rural Roads | 11.17 | 8.35 – 13.98 | <0.001 |
| VMT Per Capita | 0.01 | 0.01 – 0.01 | <0.001 |
| Active IM Program? (lagged 5 years) | -1.2 | -1.97 – -0.42 | 0.003 |
| Dependent Variable: | Fatalities/100,000 Population |
| Observations: | 361 |  |  |
| R2 / R2 adjusted | 0.716 / 0.709 |  |

# DISCUSSION

Our preliminary results show that the presence (or absence) of a vehicle safety inspection program in a U.S. state has a negative correlation to the population adjusted number of fatalities caused by motor accidents involving vehicles registered in that state. Moreover, they show that the ability of vehicle inspections to reduce road fatalities can potentially last for up to seven years. Conversely, our results point to that the negative effects of repealing an I/M program may also last for several years, and that as such, analyses of the relationship between road fatality rates and I/M programs should consider these long-term effects in order to fully capture the correlation.

These results also show that further analyses are required to explain findings surrounding some other regressor variables. For example, both models we constructed appear to show that in states and years where inclement weather was  recorded more often, or where vehicle speeding was recorded more often, the adjusted fatality rate was lower. One possible reason for this may be that the resolution of these data in the FARS dataset are very low, and these fields are populated more accurately by first responders in some states than others. Alternatively, it could be that some part of the effects of these variables are already being captured by another variable or an externality. In the future, we intend to add more regressors to our model, to potentially better explain these trends, and to improve models’ fit overall (i.e., to improve the R2  value, a measure of the proportion of data which are correctly explained by our model).

Through the development of these models, we wish to quantify the impact of establishing or repealing vehicle safety inspection programs, allowing legislators to quantitatively estimate the impact of policy-changes on road fatalities in their specific jurisdiction or state, and thus better gauge the cost-effectiveness of I/M programs as a means of preventing road fatalities, in comparison to other possible policy interventions with the same aim.

# ACKNOWLEDGEMENTS

We thank Prof. Mitchell Small for providing thoughtful feedback on the econometric tools and statistical methods used to develop our models.  We also thank Dr. Dana E. Peck and Prof. Paul S. Fischbeck, for early work in framing the problem statement of this study.

# REFERENCES

- Garbacz, C. (1990) ‘How effective is automobile safety regulation?’, Applied Economics, 22(12), pp. 1705–1714. doi: 10.1080/00036849000000076.

- Hoagland, A. and Woolley, T. (2018) ‘It’S No Accident: Evaluating the Effectiveness of Vehicle Safety Inspections’, Contemporary Economic Policy, 36(4), pp. 607–628. doi: 10.1111/coep.12284.

- Loeb, P. D. (1990) ‘Automobile safety inspection: further econometric evidence’, Applied Economics.  Chapman & Hall Ltd. , 22(12), pp. 1697–1704. doi: 10.1080/00036849000000075.

- Loeb, P. D. and Gilad, B. (1984) ‘The efficacy and cost-effectiveness of motor vehicle inspection. A state specific analysis using time series data.’, Journal of Transport Economics & Policy, 18(2), pp. 145–164.

- Merrell, D., Poitras, M. and Sutter, D. (1999) ‘The Effectiveness of Vehicle Safety Inspections: An Analysis Using Panel Data’, Southern Economic Journal, 65(3), p. 571. doi: 10.2307/1060816.

- National Highway Traffic Safety Administration (2016) ‘Fatality Analysis Reporting System ( FARS ) Analytical User ’s Manual’, (October), p. 590. Available at: https://crashstats.nhtsa.dot.gov/Api/Public/Publication/812315.

- Sutter, D. and Poitras, M. (2002) ‘The Political Economy of Automobile Safety Inspections’, Public Choice. Kluwer Academic Publishers, 113(3/4), pp. 367–387. doi: 10.1023/A:1020843328626.